## Slide 1
Survey Basics and Longitudinal Profile

## Slide 2: Survey basics - Introduction
Stream Survey Equipment
Total Station
Hand Level
Dumpy Level
GPS Survey
Laser Level
Tape Measure

## Slide 3: Survey basics - Introduction
Stream Survey Equipment
Total Station
  Slope
  Elevation
  Data Collector

## Slide 4: Survey basics - Introduction
Stream Survey Equipment
Hand Level
Dumpy Level
  Hand Held
  Quick to use
  Cheap
  Not as accurate
  Need 2 People
    1 for Rod & 1 for Level

## Slide 5: Survey basics - Introduction
Stream Survey Equipment
GPS Survey
  Consultant
  High accuracy
  Elevation
  Slope
  Angle
  Reserve for complicated sites
  Be on-site when survey is performed

## Slide 6: Survey basics - Introduction
Stream Survey Equipment
Laser Level
  Transmitter & Receiver
  Most are self leveling
  Some can do slope
  Can be used by one person
  Sight limitations
    Vegetation, slope & elevation
    Need to be able to see the Transmitter

## Slide 7: Survey basics - Introduction
Stream Survey Equipment
Measuring Rods
  Tenths vs. Feet
Tape Measure
  Recommend 200 ft. tape
Field Books
  Write everything down in the field.
Flagging, Stakes, Hammer, Marker, Paint, etc.

## Slide 8: Survey basics - Terms
Benchmark (BM) – A point of known or assumed permanent elevation.
  Brass pin, nail in a tree, or cap in concrete
  A lone metal stake
Turning Point (TP) – A point on which the elevation is determined in the process of leveling, but which is no longer needed after necessary readings have been taken.
  Should be located on a firm object such as a stone, fence post, etc.
NRCS Part 650 Engineering Field Handbook
Chapter 1 - Surveying

## Slide 9: Survey basics - Terms
Backsight (BS) - A rod reading taken on a point of known elevation. It is the first reading taken on a Benchmark or Turning Point.
Foresight (FS) – Rod reading taken on any point on which an elevation is to be determined. Only one BS is taken during each setup. All other readings are FS.
NRCS Part 650 Engineering Field Handbook
Chapter 1 - Surveying

## Slide 10: Survey basics - Terms
Height of Instrument (HI) – The elevation of the line of sight. Determined by adding the BS rod reading to the known elevation of the Point on which the BS was taken.
Side Shot (SS) – A reading to locate a point that is off the traverse or that is not intended to be used as a base of the survey. Usually to determine position of object to reference on drawing.
NRCS Part 650 Engineering Field Handbook
Chapter 1 - Surveying

## Slide 11: Survey basics - Terms
Longitudinal Profile (Long-Pro) – Typically measured from upstream to downstream in the channel thalweg, characterizes the average stream slope and depths of riffles, pools, runs, glides, step/pools.
Cross Section (CS) – Profile made perpendicular to the center line of the survey, extending a sufficient distance on each side of the center line to provide a view of the surrounding terrain.
NRCS Part 650 Engineering Field Handbook
Chapter 1 - Surveying

## Slide 12: Survey basics – Laser level
Choosing Location
-Site Distance
Set-Up & Leveling
-Solid Ground – No Movement!
Rod Assembly
-Securely Attach Receiver

## Slide 13: Survey basics – Laser level
Setting Up Field Book
Record Site Location
Project Name
Address
People Present & Task
Date
Field Conditions
Equipment Used
North Arrow

## Slide 14: Some suggestions on taking field survey notes
Concise, yet complete
  Who, where, when, etc…
  Shoot a benchmark and document location (photo helps)
  Record Height of Instrument (HI)
  Every survey point needs 3 pieces of information
    Distance on tape / station (ST)
    Foresight / rod reading (FS)
  Note (describe what your data point represents)
More to come next week in the field!!

## Slide 15: Stream morphology
Fluvial Processes and channel characteristics for longitudinal survey

## Slide 16: Stream morphology
Slope dictates dominant bedform type and length and spacing of bed features
step / plunge pool
6.1 %
‘pocket-water’
3.2 %
riffle / pool
1.2 %

## Slide 17: Energy dissipation mechanism varies by slope….
High-gradient vertical (plunge pools)
Low-gradient floodplain
Wildland Hydrology

## Slide 18: Slope is the key
Channel Slope
  dictates dominant bedform & grade controls
  drives bed shear and entrainment
  Maintains substrate transport and stability
  (balance)
  As channel slope increases…
    channels become less sinuous
    energy dissipation more vertical
    grade control more frequent and robust

## Slide 19: Natural grade control maintains channel slope and stability.

## Slide 20: Slope is the key.
concave
uniform
convex
concave/convex
potential headcut
Zone of deposition
potential headcut
Zone of deposition
ideal, preferred setting
vertical offset

## Slide 21: Geomorphic site assessment is essential for success.
  If we don’t know what’s broken, how can we fix it?
    A different way of thinking (what does the stream need?)
  Continuity, functionality, and longevity (not just replace, but maintain)
Wildland Hydrology

## Slide 22: Longitudinal Profile
Slope of upstream and downstream channels
Existing invert elevations
Type, spacing, and length of bed features
Grade controls
  - Relative stability (tie-in points)
Pool depth
Road-surface elevations
  - Minimum coverage over new culvert

## Slide 23: Key bed features
- Steps and Pools
- Riffles and Pools
- Large Woody Debris
- Transverse Ribs
- Particle Clusters
- Gravel Bars
step
step
step
step
pool
pool
pool
pool
riffle
riffle
pool
riffle crest
pool
riffle
riffle crest
pool
transverse rib
particle cluster

## Slide 24
Transitional points along the channel profile
Riffle crests
Top and base of steps, cascades & LWD
Bed feature between grade control crests (one point at minimum)
Rock clusters (‘key pieces’) or transverse ribs (extended riffles & ‘pocket water’)
Other notable features (bedrock, etc.)
Typical Measuring Points for Longitudinal Profiles

## Slide 25: Connecting the dots…
Objective is to re-establish channel continuity
  minimize channel adjustment (erosion and sedimentation)
  increase longevity of the new crossing (flood resiliency)
  maintain AOP
Plunge pool disrupting continuity

## Slide 26: Pools matter, too…
FLOW
6”
24”
riffle crest
pool
riffle crest
pool
CULVERT INVERT
Bedform variability
  Vertical adjustment potential
  Needed for streambed stability and AOP
  Influences structure bury depth, structure type, bottom vs. bottomless
Notes: Introduce project partners

## Slide 27: Stability of grade controls
Needed to inform tie-in points
  Rate relative stability (good, moderate, poor)
  Based on what’s typical
  Use your best judgement
Woody debris
Rock cluster

## Slide 28: Questions ?