## Slide 1
Structural
Infiltration Practices

## Slide 2
Structural Infiltration Practices
Introduction
Practices
DGLVR Project Examples

## Slide 3
What is “infiltration”:
Any practices that encourage water to soak into the ground instead of running off.
Infiltration Practices
Introduction

## Slide 4
Infiltration Practices
Introduction
“Traditional Practices”: Collection over infiltration
Roller curb berms
X
X

## Slide 5
Infiltration Practices
Introduction
Remember
our hillside?
Infiltration over runoff is a Program Focus (road fill, pipes, underdrain, etc.).
What happens in the real world….

## Slide 6
Infiltration Practices
Introduction
Remember
our hillside?
Infiltration over runoff is a Program Focus (road fill, pipes, underdrain, etc.).
What happens in the real world….
Sometimes the situation requires more “structural” infiltration practices

## Slide 7
Structural Infiltration practices:
Structures that capture stormwater runoff and allow it to slowly seep into the soil.
Applicable for urban, suburban, and rural roads.
Often most beneficial in densely developed areas and agricultural landscapes.
Alleviate flooding and erosion, reduce surface water pollution, and promote groundwater recharge.
Infiltration Practices
Introduction

## Slide 8
Structural Infiltration practices:
Infiltration Practices
Introduction
Infiltration Basin
Rain Garden
Detention Basin
Infiltration Trench
Infiltration Swale
Any structure designed to capture stormwater runoff and allow it to slowly seep into the soil.
Examples: too many types and sizes to cover them all
Stilling Basin
Bio-Swale
Grassed Waterway
Permeable Pavement
Constructed Wetland

## Slide 9
Infiltration Practices
Introduction
Geology, Soils, and Infiltration rates vary widely across PA.
Analysis may be needed to determine infiltration rates.

## Slide 10
Disclaimer #1
ENGINEERING / DESIGN (and permits) may be needed, depending on structure, location, and size.
Conservation District can help determine if an engineer or design is needed.
Infiltration Practices
Introduction

## Slide 11
Disclaimer #2
Practices are customizable and vary based on site conditions.
This entire training could be on infiltration. These are examples only.
Purpose is to show ideas of what might be possible through DGLVR!
Infiltration Practices
Introduction

## Slide 12
Structural Infiltration Practices
Introduction
Practices
DGLVR Project Examples

## Slide 13
Structural Infiltration Practices
Infiltration Beds / Trenches
Infiltration Basins
Vegetated Swales
Rain Gardens
Subsurface Structures
Infiltration Practices
This is not all-inclusive

## Slide 14
Typical from PA Stormwater BMP Manual
Infiltration Bed Detail
Infiltration Practices
Infiltration Beds / Trenches
When sized appropriately, stone beds can be used at outlet of individual pipes and turnouts or at the terminal outlet of a storm sewer system.
Pipe Outlet

## Slide 15
Infiltration Practices
Infiltration Bed used on rural storm sewer in agricultural area.
Bed located prior to discharge to headwater channel of valley stream.
Infiltration Beds / Trenches
Pipe Inlet

## Slide 16
Infiltration Bed
(3’D x 20’L x 7’W)
3’ Deep, filled w/ R4 and edged with pallet stone.
Infiltration Practices
Infiltration Beds / Trenches
15” Pipe Outlet

## Slide 17
Infiltration Practices
Infiltration Beds / Trenches
2
3
1
3’ Deep, filled w/ R4 and edged with pallet stone.

## Slide 18
Infiltration Practices
Infiltration Beds / Trenches
Over time Infiltration Bed blends in but continues to function as intended to reduce water and sediment leaving the road.
Infiltration Bed
(3’D x 20’L x 7’W)
15” Pipe Outlet
7 years later

## Slide 19
Infiltration Trench
Infiltration Practices
Infiltration Beds / Trenches
Similar to infiltration bed, but longer and on contour (virtually flat)

## Slide 20
Structural Infiltration Practices
Infiltration Beds / Trenches
Infiltration Basins
Vegetated Swales
Rain Gardens
Subsurface Structures
Infiltration Practices
This is not all-inclusive

## Slide 21
Infiltration basin: A depression that temporarily stores stormwater and allows it to seep into the soil.
Infiltration Basin
Infiltration Practices
Typical features:
Forebay or Stilling Basin
Storage Pool
Pool Level Riser
High-water Spillway
Incorporated Underdrain
Easily Maintained
Not all infiltration basins have all the above features
https://stormwaterbook.safl.umn.edu/infiltration-practices

## Slide 22
Infiltration basin: A depression that temporarily stores stormwater and allows it to seep into the soil.
Infiltration Basin
Infiltration Practices
Practical Uses:
Upslope of road to intercept water
At ditch outlets
At storm sewer discharge
Before storm sewers to reduce flows
*situations often call for site specific innovation
https://stormwaterbook.safl.umn.edu/infiltration-practices

## Slide 23
Infiltration Basins: “Teardrops” for individual pipe outlets
Infiltration Practices
Infiltration Basin - Teardrop

## Slide 24
R3 riprap
Designed Overflow
Ditch/Pipe Flow
Infiltration Practices
Earthen Bottom
Infiltration Basin - Teardrop
Infiltration Basins: “Teardrops” for individual pipe outlets

## Slide 25
R3 riprap
Designed Overflow
Ditch/Pipe Flow
Infiltration Practices
Teardrop
Infiltration Basin - Teardrop
Infiltration Basins: “Teardrops” for individual pipe outlets

## Slide 26
Infiltration Practices
Must be maintained, especially on gravel roads.
Infiltration Basin - Teardrop
Year 1
Year 5
After Cleanout
Full of sediment

## Slide 27
Infiltration Basins: for Off-right-of-way flow coming to road
Infiltration Basin - Off-ROW
Infiltration Practices
Stormwater basin collects and infiltrates runoff from an upslope park and slowly discharges storm flow.
Road
Overflow to road ditch

## Slide 28
Infiltration Practices
Basin infiltrates runoff from farm fields and overflows to grass swale
Road
Infiltration Basin - Off-ROW
Infiltration Basins: Can go above road for off-ROW water

## Slide 29
Infiltration Practices
Infiltration Basin - Off-ROW
Infiltration Basins: Can go in ditch for road runoff
Use when ditch outlets are not feasible, and space is available.
Basins can be in a series to:
Slow ditch drainage
Limit runoff
Capture sediment
Design to be easily maintained from the road.
Infiltration Basin
overflow

## Slide 30
Infiltration Practices
Infiltration Basin - Off-ROW
Infiltration Basins: Can go in ditch for road runoff
Infiltration Basin

## Slide 31
Infiltration Practices
Infiltration Basin - Off-ROW
Infiltration Basins: Can go in ditch for road runoff
Infiltration Basin
overflow

## Slide 32
Infiltration Practices
Infiltration Basin - Off-ROW
Infiltration Basins: Can go at pipe or storm sewer outlet
overflow

## Slide 33
Infiltration Practices
Infiltration Basin - Off-ROW
Infiltration Practices
Infiltration Basin
Infiltration Basin – Storm Sewer
Infiltration Basin
Storm Sewer Outlets from two streets
Outlet
Infiltration Basins: Can go at pipe or storm sewer outlet

## Slide 34
Infiltration Practices
Infiltration Basin – Storm Sewer
Outlet riser
Large basin collects water from two roads and parking lot

## Slide 35
Structural Infiltration Practices
Infiltration Beds / Trenches
Infiltration Basins
Vegetated Swales
Rain Gardens
Subsurface Structures
Infiltration Practices
This is not all-inclusive

## Slide 36
Infiltration Practices
Vegetated Swale
Vegetated Swales: Filter and slow runoff, promote infiltration

## Slide 37
Infiltration Practices
Vegetated Swale
Vegetated Swales: Filter and slow runoff, promote infiltration
BEFORE
AFTER
Could not get drainage outlets
Ditch continually eroding
Check dams installed to slow flow
Ditch seeded and mulched

## Slide 38
Vegetated Swales: Filter and slow runoff, promote infiltration
Infiltration Practices
Vegetated Swale
Road
Storm Sewer Outlet

## Slide 39
Vegetated Swales: Filter and slow runoff, promote infiltration
Infiltration Practices
Vegetated Swale
DURING
AFTER
Road
Road
Storm Sewer Outlet
Storm Sewer Outlet

## Slide 40
Structural Infiltration Practices
Infiltration Beds / Trenches
Infiltration Basins
Vegetated Swales
Rain Gardens
Subsurface Structures
Infiltration Practices
This is not all-inclusive

## Slide 41
Rain Gardens
A depressed area in the landscape that collects stormwater from streets and roads to promote infiltration.
Vary widely in size and shape.
Typically planted with native vegetation
Typically used in more urban settings
Infiltration Practices
Storm flow from road
Rain Garden
Riser for overflow discharge

## Slide 42
Infiltration Practices
Infiltration Basin – Rain Garden
Rain Garden: A depressed area in the landscape that collects stormwater from streets and roads to promote infiltration.
BEFORE
Proposed rain garden
Drop inlet drains to stream
Cherry Lane, Lancaster County

## Slide 43
Infiltration Practices
Infiltration Basin – Rain Garden
AFTER
Rain Garden
Cherry Lane, Lancaster County
Rain Garden: A depressed area in the landscape that collects stormwater from streets and roads to promote infiltration.

## Slide 44
Infiltration Practices
Drainage from both sides of road is directed to a roadside rain garden. Overflow outlets to the storm sewer.
Infiltration Basin – Rain Garden
Easterly Parkway Rain Gardens, Centre County

## Slide 45
Infiltration Practices
Native vegetation and weirs are used to slow flow and utilize water.
Infiltration Basin – Rain Garden
Easterly Parkway Rain Gardens, Centre County

## Slide 46
Infiltration Practices
Rain Garden
Maybe get better pictures, or use different project?
Everhart Street, Chester County

## Slide 47
Infiltration Practices
Rain Garden
Everhart Street, Chester County
Outlet Riser
Maybe get better pictures, or use different project?

## Slide 48
Structural Infiltration Practices
Infiltration Beds / Trenches
Infiltration Basins
Vegetated Swales
Rain Gardens
Subsurface Structures
Infiltration Practices
This is not all-inclusive

## Slide 49
Infiltration bed below road - Montgomery County
Pervious Pavements
Infiltration Practices
Notes: Clean up this slide and add “Urban Drainage Issues”

## Slide 50
Infiltration Practices
Pervious Pavements
Reynolds Ave, Lancaster County 3/3
Infiltration bed for porous pavement

## Slide 51
Infiltration Practices
Pervious Pavements
Reynolds Ave, Lancaster County 1/3
AFTER
BEFORE

## Slide 52
Infiltration Practices
Pervious Pavements
Pervious Pavement allows water to seep through the road surface to be absorbed by underlying soils.
Pervious Pavement
Porous Rock
Cahill and Associates

## Slide 53
Hoopes Alley, Chester County
Infiltration Practices
Pervious Pavements
Stream
Pavers in sand over porous rock bed allows infiltration

## Slide 54
Infiltration Practices
Pervious Pavements
All pervious pavements require more specialized maintenance.
Porous Surface will clog over time. How long depends on the amount of loose material: dirt, leaves, salt, cinders.
Specialized vacuum trucks or street sweepers often needed.
https://3rpsinc.com/porous-pavement-sweeping/

## Slide 55
Structural Infiltration Practices
Introduction
Practices
DGLVR Project Examples

## Slide 56
AFTER
Project Walkthrough: Bradford County, Moore Hill Road
2016: $77K Grant, $26K in-kind
Road runoff eroding ditch to PennDOT road and stream
Infiltration swale constructed through field

## Slide 57
Infiltration Practices
Vegetated Swale
Runoff cut eroded ditch through farm field, flooded PennDOT road, and entered stream
BEFORE
BEFORE
Bradford, Moore Hill 2/5
Low-gradient infiltration swale through field for road runoff

## Slide 58
Infiltration Practices
Vegetated Swale
Moore Hill Road, Bradford County
Long and wide swale at a low gradient
Energy dissipater and/or infiltration bed
Eroded ditch filled in
BEFORE
AFTER
“Virtually Flat” drivable Infiltration Swale

## Slide 59
Infiltration Practices
Vegetated Swale
Moore Hill Road, Bradford County
Drivable or mowable shape
DURING
After
Dense vegetation slows, filters, and utilizes stormwater
Bradford, Moore Hill 4/5
Low-gradient infiltration swale through field for road runoff

## Slide 60
Infiltration Practices
Vegetated Swale
Moore Hill Road, Bradford County
Dense vegetation slows, filters, and utilizes stormwater
Bradford, Moore Hill 5/5
Low-gradient infiltration swale through field for road runoff

## Slide 61
AFTER
Project Walkthrough: Venango County, Wood Rd
Excessive road runoff to single outlet
Installed forebay to grass swale to infiltration basin.
BEFORE

## Slide 62
Infiltration Practices
Example Project
Forebay
Grass swale
Infiltration Basin
Overflow back to road culvert

## Slide 63
Infiltration Basin
Forebay
Grass swale
DURING
Venango, Wood Rd 3/6
Stormwater outlet to forebay, to grassed swale, to infiltration basin
Picture taken from road edge

## Slide 64
Infiltration Basin
Forebay
Grass swale
DURING
Venango, Wood Rd 4/6
Stormwater outlet to forebay, to grassed swale, to infiltration basin
Road

## Slide 65
Infiltration Basin
If basin fills, outlets excess to new crosspipe
DURING
Venango, Wood Rd 5/6
Stormwater outlet to forebay, to grassed swale, to infiltration basin

## Slide 66
Infiltration Basin
Forebay
Grass swale
AFTER
Venango, Wood Rd 6/6
Stormwater outlet to forebay, to grassed swale, to infiltration basin
Picture taken from road edge

## Slide 67
AFTER
Project Walkthrough: Westmoreland County, Newhouse Park Rd
2022: $123K Grant, $22K in-kind
Parking lot runoff washing out road.
Collected runoff in storm sewer.
Directed runoff to forebay (for cleanout) and detention basin
BEFORE

## Slide 68
BEFORE
BEFORE
Edge of parking lot
Drains to storm sewer to stream
Westmoreland, Newhouse 2/9
Berm to collect parking lot and road runoff
Direct runoff to forebay (for cleanout) and detention basin

## Slide 69
BEFORE
AFTER
Collect water from parking lot
Forebay (for cleanout)
Detention Basin
Storm Sewer

## Slide 70
Collect water from parking lot
Forebay (for cleanout)
Storm Sewer
Detention Basin
AFTER
Collect water from parking lot
Forebay (for cleanout)
Detention Basin
Storm Sewer
Engineered Plan

## Slide 71
New Stormwater Inlet
Paved grade break forces water into inlet
BEFORE
AFTER
Westmoreland, Newhouse 5/9
Berm to collect parking lot and road runoff
Direct runoff to forebay (for cleanout) and detention basin
township paved parking lot as in-kind

## Slide 72
AFTER
New Stormwater Inlet
Westmoreland, Newhouse 6/9
Berm to collect parking lot and road runoff
Direct runoff to forebay (for cleanout) and detention basin

## Slide 73
Westmoreland, Newhouse 3/4
Installation of detention basin to catch runoff from parking lot and road.
Getting before/during pics from Rob
Parking Lot
Discharged to forebay for cleanout
AFTER
Paved grade break forces water into inlet
New Stormwater Inlet

## Slide 74
Detention Basin
AFTER
Storm Sewer Outlet
Forebay
Westmoreland, Newhouse 8/9
Berm to collect parking lot and road runoff
Direct runoff to forebay (for cleanout) and detention basin

## Slide 75
AFTER
Detention Basin
Forebay
Road
Westmoreland, Newhouse 9/9
Berm to collect parking lot and road runoff
Direct runoff to forebay (for cleanout) and detention basin
Road

## Slide 76
AFTER
Project Walkthrough: Westmoreland County, Shields Farm Rd
2018: $49K Grant, $11K in-kind
Road collected all runoff from long hill
Installed detention basin
Installed several crosspipes, through the bank pipes, and infiltration trenches

## Slide 77
BEFORE
Westmoreland, Shields Farm 2/8
Detention Basin on upper site
Crosspipes, through-the-bank pipes, and infiltration basins on bottom of site

## Slide 78
BEFORE
AFTER
New
Detention
Basin
Overflow outlet
Crosspipe, to
Through the bank pipe, to
Infiltration Trenches

## Slide 79
AFTER
New
Detention
Basin
Overflow outlet
Pipes to infiltration trenches
New
Detention
Basin

## Slide 80
AFTER
New
Detention
Basin
Overflow outlet
Pipes to infiltration trenches
Infiltration Trenches
Westmoreland, Shields Farm 5/8
Detention Basin on upper site
Crosspipes, through-the-bank pipes, and infiltration basins on bottom of site
inlet

## Slide 81
Outlet Pipe
Infiltration Trench
Courtesy Westmoreland
Conservation District
Infiltration Trenches
(on contour)
Westmoreland, Shields Farm 6/8
Detention Basin on upper site
Crosspipes, through-the-bank pipes, and infiltration basins on bottom of site
Infiltration trench size is site dependent
This one is 3’ x 3’ x 50’
on contour

## Slide 82
Infiltration Trenches
(on contour)
Westmoreland, Shields Farm 7/8
Detention Basin on upper site
Crosspipes, through-the-bank pipes, and infiltration basins on bottom of site
AFTER

## Slide 83
AFTER
BEFORE
AFTER
Infiltration Trenches
Westmoreland, Shields Farm 8/8
Detention Basin on upper site
Crosspipes, through-the-bank pipes, and infiltration basins on bottom of site

## Slide 84
AFTER
Project Walkthrough: Montgomery County, Webber Rd
2016: $24K Grant, $2K in-kind
Badly eroded ditch along suburban road.
Installed storm sewer, but with grass sale over top to promote infiltration

## Slide 85
Yards and drives drain to road.
Nowhere to outlet ditches.
The Problem:
Numerous house and hard drains
BEFORE
No outlets due to houses, badly eroded ditches
Montgomery, Webber Rd 2/7
Grass Swale constructed over newly installed storm sewer.

## Slide 86
Site Plan:
Drop inlets and storm sewer
Grassed swale over storm pipes to promote infiltration and alleviate landowner concerns
Montgomery, Webber Rd 3/7
Grass Swale constructed over newly installed storm sewer.

## Slide 87
BEFORE
Eroded Ditch
Montgomery, Webber Rd 4/7
Grass Swale constructed over newly installed storm sewer.

## Slide 88
BEFORE
DURING
Eroded Ditch
Montgomery, Webber Rd 4/7
Grass Swale constructed over newly installed storm sewer.

## Slide 89
BEFORE
DURING
AFTER
Eroded Ditch
Grass Swale
Drop Inlets
Montgomery, Webber Rd 4/7
Grass Swale constructed over newly installed storm sewer.

## Slide 90
Storm Sewer Inlet
AFTER
Storm Sewer Inlets
Grass Swale
Montgomery, Webber Rd 5/7
Grass Swale constructed over newly installed storm sewer.

## Slide 91
Storm Sewer Inlets
Grass Swale over storm sewer
Storm Sewer Inlets
AFTER
Montgomery, Webber Rd 6/7
Grass Swale constructed over newly installed storm sewer.

## Slide 92
Constant ditch washouts, erosion into yards
BEFORE
AFTER
Grass Swale over storm sewer
Storm Sewer Inlets
Trees removed
Montgomery, Webber Rd 7/7
Grass Swale constructed over newly installed storm sewer.

## Slide 93
AFTER
Project Walkthrough: Lancaster County, North Lane
2019: $14K Grant, $3K in-kind
Stormwater in borough piped to stream
Rain garden installed to filter sediment and infiltrate runoff
BEFORE
Paved swale piped to stream

## Slide 94
BEFORE
PLAN
Lancaster, North Lane 2/4
Rain garden installed between road and walking trail before stream.

## Slide 95
Rain Garden
Overflow Outlet
DURING
Lancaster, North Lane 3/4
Rain garden installed between road and walking trail before stream.

## Slide 96
Rain Garden
Overflow Outlet
AFTER
Lancaster, North Lane 4/4
Rain garden installed between road and walking trail before stream.

## Slide 97
AFTER
Project Walkthrough: Dauphin County, 31st Street
2019: $85K Grant, $0 in-kind
Road runoff washing out rail trail below into stream
Installed drop inlets to “cascading” subsurface infiltration structures
BEFORE

## Slide 98
Water from two roads ran down road, washed out rail trail and into stream
BEFORE
Dauphin, 31st St 2/7
Installed drop inlets to “cascading” subsurface infiltration structures

## Slide 99
BEFORE
AFTER
Drop Inlets
subsurface infiltration beds
Dauphin, 31st St 3/7
Installed drop inlets to “cascading” subsurface infiltration structures

## Slide 100
Road Surface
4 Drop Inlets
1/4
Dauphin, 31st St 4/7
Installed drop inlets to “cascading” subsurface infiltration structures

## Slide 101
Road Surface
2/4
4 Drop Inlets
Dauphin, 31st St 4/7
Installed drop inlets to “cascading” subsurface infiltration structures

## Slide 102
Road Surface
3/4
4 Drop Inlets
Dauphin, 31st St 4/7
Installed drop inlets to “cascading” subsurface infiltration structures

## Slide 103
4 Drop Inlets
Dauphin, 31st St 4/7
Installed drop inlets to “cascading” subsurface infiltration structures
4/4

## Slide 104
Bank of drop inlets installed at top of project to capture all runoff
Dauphin, 31st St 5/7
Installed drop inlets to “cascading” subsurface infiltration structures

## Slide 105
Excavation and filling of lower subsurface infiltration beds
Dauphin, 31st St 6/7
Installed drop inlets to “cascading” subsurface infiltration structures

## Slide 106
Drop Inlets
subsurface infiltration beds
AFTER
Dauphin, 31st St 7/7
Installed drop inlets to “cascading” subsurface infiltration structures

## Slide 107
Structural Infiltration practices:
Infiltration Practices
Introduction
Infiltration Basin
Rain Garden
Detention Basin
Infiltration Trench
Infiltration Swale
Any structure designed to capture stormwater runoff and allow it to slowly seep into the soil.
Examples: too many types and sizes to cover them all
Stilling Basin
Bio-Swale
Grassed Waterway
Permeable Pavement
Constructed Wetland

## Slide 108
next chapter:
DSA
Helpful References:
Structural Infiltration Practices
QUESTIONS?
ADDITIONAL RESOURCES:
Your Conservation District
Your Municipal Engineer
PA Stormwater Best Management Practices: Specifically chapter 6 on “Structural BMPs”
PA MS4: DEP stormwater management resources.
(Municipal Separate Storm Sewer System)